# Fasteners		  		Name ______________________________		X121

PROCEDURE:

Read the booklet titled “Fasteners” and answer the following questions.  Be sure to have your teacher quiz you and sign this sheet before you move on.

.

- On page three of the fastener book it talks about screws. Draw a side profile picture below of what the FILLISTER screw looks like.

- What is the difference between a hexagon bolt and a hexagon cap screw?

- Standard wrenches, sockets, nuts and bolt sizes increase in steps of one sixteenth (1/16”) of an inch. A standard set of wrenches come in a set of sizes below. Fill in the missing sizes.

1/4       5/16       3/8       7/16      ___     9/16       5/8       11/16      ____      13/16       7/8       15/16       1

- The direction a clock turns is called CLOCKWISE. The opposite direction is called COUNTER-CLOCKWISE. Which direction is used to tighten a nut or bolt?

- What is the purpose of a lock washer?

- What type of nut is used with a COTTER PIN?

- The Briggs & Stratton Engine used keys to keep the flywheel from spinning. Draw a picture below of what a WOODRUFF key looks like.

- The Briggs and Stratton engine uses 2 types of different threads, coarse (UNC) and fine (UNF). This refers to the pitch of the thread per inch. What is the threads per inch of a ¼ inch bolt that is labeled ¼-20-UNC?

- The connecting rod bolts are UNF (fine thread) type of bolts. What is the reason for using a UNF bolt in this application instead of a coarse UNC bolt?

- What does the M10 stand for on a metric bolt?

- What does the 1.5 stand for on a metric bolt?

- How many lines are on the head of a GRADE 8 bolt?

LAB ACTIVITY

- Ask your teacher for a ¼ - 20 – UNC bolt and nut.

- Place the nut in the vise and tighten slightly.

- Thread the bolt on until it bottoms.

- torque the bolt to 100 in/lbs using the small torque wrench 3/8 drive.

- Loosen the bolt.

- Remove the bolt, inspect the threads. Are they ok?

- If yes, reinstall into the nut and using the larger torque wrench, torque it down to 100 ft/lbs.

- Loosen the bolt.

- Remove the bolt, inspect the threads. Are they ok?

Notice what can happen if you read the torque specifications improperly?

Know the difference between in/lbs (inch/pounds) & ft/lbs (foot/pounds). Ft/lbs is 12 times higher in torque.

Now do the same procedure with a larger bolt. Ask your teacher for a ¾ - 10 - UNC

CHECK POINT__________