# Dismantling, Cleaning, and		Name _____________________________ 	X130

Identifying Engine Parts	(for the 90000/100000 series engines)

PROCEDURE:

Read the booklet “Engine Overhaul” & ask your teacher for a question.  CHECK POINT ______ 1.0 Hr

Engine Disassembly Procedure.

- Drain the oil from the engine by removing the oil plug at the bottom of the engine.  Tip the engine so all of the oil drains out into the oil container.

- Remove the blower housing.

- Drain the gasoline from the engine by first removing the carburetor and gas tank as a unit – do not take them apart.  Drain the gasoline into the red gasoline can using a funnel.

- Find a piece of cardboard about as wide as this paper and about half as high.  Stick each of your bolts through the cardboard in groups.  Label each group of bolts with their location so that you can identify them later.

- Remove the cylinder head.

- Identify the four strokes for your teacher, and be prepared to explain each one.

CHECK POINT _________ 1.0 Hr.

- Remove the flywheel nut using the flywheel holding tool and the 15/16” socket with the flex handle as demonstrated by your teacher - ask for help if needed.

- Remove the flywheel.

- Do not lose the flywheel key - a small piece of aluminum that keeps the flywheel and crankshaft rotating together.

- Remove the magneto coil (2 small bolts)

- Remove the muffler (2 bolts)

- Remove the side cover (6 bolts)

- Remove the camshaft by pulling it outward.

- Remove the 2 valve lifters (if they haven’t already fallen out).

- Slide the piston to the bottom of its stroke, and remove the connecting rod bolts.  These bolts are different from the side cover bolts because the thread on the bolt is finer.

- Remove the oil dipper.

- Remove the connecting rod cap – keep in mind that the connecting rod cap only fits on one way.  If it is installed the wrong way, it can do damage to the engine.

- Slide the piston out of the top of the motor.

- Point out the following items to your teacher:

  - All of the bolts are organized, grouped, and clearly labeled in your piece of cardboard.

  - Connecting rod bolts are different from the bolts that hold the sump cover on - they have a finer 	thread.

  - The connecting rod cap only fits on one way.  There are tabs on both the cap and the 	connecting rod that allow it to be installed properly.

CHECK POINT _________ 1.0 Hr.

- Remove both valves using the valve spring compressor tool as demonstrated by your teacher.

- Clean all oily parts in the solvent tank.  Do not clean ignition parts, the blower housing, or carburetor / gas tank assembly.

- Dry all cleaned parts using compressed air.  BE SURE TO WEAR SAFETY GLASSES WHEN BLOWING ANYTHING OFF WITH COMPRESSED AIR.

- Organize all of your parts on your CLEAN work table or counter and be prepared to identify the names of all of the following parts:

  - _____ Carburetor		_____ Flywheel Key		_____ Gas Tank

  - _____ Valve Keepers		_____ Blower Housing	_____ Flywheel

  - _____ Cylinder Block		_____ Muffler			_____ Piston

  - _____ Connecting Rod	_____ Connecting Rod Cap	_____ Connecting Rod Bolts

  - _____ Magneto Coil		_____ Valve Springs		_____ Valve Cover

  - _____ Crankshaft		_____ Camshaft		_____ Lifters

  - _____ Intake Valve		_____ Exhaust Valve		_____ Cylinder Head

  - _____ Cylinder Head Gasket	_____ Oil Dipper		_____ Spark Plug

CHECK POINT __________ 2.0 Hr