Antifreeze Solutions				X185

Information:

Antifreeze (Ethylene Glycol) is added to the water in a cooling system to lower its freezing point and thus ensure that the coolant may flow from the radiator to the engine block during cold weather.

Reference:

- CDX eTextbook – Engines – Engine cooling

- Automotive Mechanics – Chapter 25 & 26 pg. 315-327 & 328-339.

Tools and Equipment:

- Coolant hydrometer.

- Sample bottles of antifreeze solutions.

Procedure:

- Using the hydrometer draw up sufficient solution to fill the graduated chamber.

- When it is full pinch or bend the tube to prevent spillage.

- Tap the chamber to release air bubbles on the gauge needle.

- Using the above procedures determine the freezing point of solutions 1 through 8.

- _____________

- _____________

- _____________

- _____________

- _____________

- _____________

- _____________

- ____________

Assignment:

- What does a coolant hydrometer measure?

- Should ethylene glycol be used full strength in a cooling system? If not, why not?

- What is the maximum water to ethylene glycol ratio that should be used?

Check Point _________1.0 hr