Remove and Replace a Cylinder Head		X190

Information:

Nearly all engines have removable cylinder heads.  This enables service work in connection with the valves and pistons to be done with a greater degree of ease and dispatch.

Reference:

- CDX eTextbook – Engines – Cylinder Heads

- Automotive Mechanics – Ch 39 p 498

Procedure:

Note: 	It is understood that the water, hose connections, spark plugs, and wires have been removed from the engine.

- Use the proper size socket and power handle to loosen the cylinder head cap screws or nuts; then, with a speed handle and socket, remove them.  Note:  If the cylinder head is not lifted straight up, it is likely to strike and damage an open valve.

- Lift the cylinder head straight up off the block.

- Carefully remove the gasket.  Take care not to bend or damage the gasket.

- Clean all carbon from the head, block and pistons.  Use a carbon scraper.

Cylinder head gaskets are capable of taking care of warpage up to eight thousands of an inch (.008”).  A cylinder head warped more than this should be replaced.

- Set the gasket in place.

- Lower the head gently into place.

- Start all the cylinder head cap screws or nuts into the threads with your fingers.

- Spin all the cap screws down with a speed handle until they touch the head.

- With a torque wrench tighten the cap screws or nuts to the proper torque and in the proper order (above).

  - First torquing – 30 ftlbs

  - Second torquing – 45 ftlbs

  - Third torquing – 60 ftlbs

  - Final torquing – 60 ftlbs

Assignment:

- Why should the cylinder head cap screws or nuts be tightened evenly?

- Why should the centre cap screw be tightened first?

- Why is copper and asbestos use in the manufacture of cylinder head gaskets?

- Why are engines equipped with removable cylinder heads?