# Starting and Stopping an Engine    Name _____________________________   X122

PROCEDURE:

A. Read the booklet “Briggs & Stratton Manual” (pages 1 – 9) and answer the following questions:

1. List 4 safety precautions (DO NOT…) that should be followed when starting / running an engine.

a.)

b.)

c.)

d.)

2. What viscosity oil should be used in warm temperatures (above 10 degrees Celsius)?

3. What is the crankcase oil capacity?

4. What are 2 reasons why Briggs & Stratton does not recommend ethanol blended gasoline?

5. Why should the choke be used when starting a cold engine (what is the purpose of a choke)?

6. What is the factory set governed idle speed?

7. How often should the oil level be checked?

8. How often should the oil be drained / refilled?

9. What is the result of running an engine at high speeds when not required?

10. How much oil should be placed in the cylinder if an engine is stored for long periods of time, and why 	is this oil placed there?

B. Engine Starting and Stopping.

- Remove the spark plug, and check for spark and compression as demonstrated by your teacher

- Re-install the spark plug.  Do not over-tighten the spark plug, as this will strip the threads in the 		cylinder head.

- Fill the crankcase with oil by pouring oil through a funnel into the oil port until it is full.  Once it 	is full it will show full on the dipstick, so pour slowly and carefully.  Clean up any spills.

- Fill the gas tank until it is half full.

- Connect the exhaust hose – have your partner hold the hose in place.

CHECK POINT _________

6. Pull the cord its full length quickly and sharply until the engine starts.

7. Stop the engine by grounding the spark plug to the cylinder head as demonstrated by your teacher.

CHECK POINT _________