Jacking Up a Car and Placing Safety Stands Under It		X179

Equipment:

Floor Jack

4 Safety Stands

Information:

First of all you must become familiar with the jack; be able to find the following:  the release valve, the handle, and the raising platform.  When lifting a car with a jack, caution must be used when positioning it under the car.  Serious damage could result from positioning the jack improperly.  Many parts underneath a car are too weak to support the weight of a car.  The following simple diagram will show the proper portions of the undercarriage to “lift” against.

- To raise the front of the car, place the raising platform under the centre of the front cross member at point 1.

- To raise the rear of the car, place the raising platform under the centre of the rear axle at point 2.

- To raise one side of the car at the front, under the control arm at the front spring at points 3.

- To raise one side of the car at the rear, under the rear axle at points 4.

Procedure:

The car is to be jacked up one end at a time, starting with either the front or the back.

- Place the jack directly under the part to be raised.

- Close the release valve and raise the jack platform to touch the car.

Caution:  Make sure that the jack is not touching on any steering parts, oil pan, gas tank, drive shaft, gas or brake lines muffler etc.

- Continue jacking until the car is at the desired height or until safety stands can be put into position.  At the front place 2 safety stands (one on each side) at position 3, while at the rear place the stands at positions 4.

- Turn the release knob slowly to allow the car to settle or lower gently onto the safety stands.

- Check the safety stands to make sure that they are safely in place and that the car will not slip off.

- Repeat the above operations at the other end of the car, and then have the teacher inspect your work.

- Again lift the car and remove the safety stands, one end of the car at a time.

Check Point ___________