Reconditioning a Screwdriver						X181

Tools, Materials and Equipment

- Bench Grinder

- Safety Goggles

- Small Container of Water

- Screwdriver		(check with instructor)

References:

- CDX eTextbook – Tools and Equipment

Procedure:

- Make sure Grinding Wheel is properly “dressed”

- By holding the screwdriver tip squarely to the grinding wheel, square off the tip.   Fig. 1 (Cool the tip often to avoid overheating

- Grind screwdriver face at original angle.  Hold screwdriver handle in right hand and apply light pressure on screwdriver face with index finger of left hand.  Fig. 2.

- Check with instructor.

Check Point _____________