Single and Double Flaring		X188

Tools, Materials and Equipment:

- Flaring tool kit

- Tubing cutters

- Tubing (see instructor)

- Flat file

References:

- CDX eTextbook – Tools and Equipment – Pipe flaring and cutting\

- Automotive Mechanics – Ch

Procedure:

Cutting

- Select a piece of tubing that is  perfectly straight, round and without kinks

- Cut a 4” length of tubing, using the tubing cutter.  Holding the tubing in left hand, operate the cutter with right.  Tighten the hand nut on the cutter lightly , rotate cutter several revolutions, tighten the nut again.  Repeat this process until tubing is cut.  CAUTION:  Do not apply too much pressure to the cutter, as this will cause the tubing to flatten, and make flaring impossible.

Single Flare

- Prepare end of tubing carefully by making sure tubing is cut off square.

- Debur inside with Reamer blade of tubing cutter.

- Chamfer the outside of tubing with file.

- Insert tubing through correct size holes so the cut end of the tubing slightly protrudes at the bevelled of flaring bar.  See figure 1.

- Tighten wing nuts securely, starting with the nut nearest the tubing.

- Place yoke assembly over flaring bar, so that cone enters the end of the tubing.

- Tighten T-handle until end of tube is pressed firmly into bevel of flaring bar.  See figure 2

- Remove yolk assembly and inspect the flare.

- Check with instructor.

Double Flaring

- Prepare the tubing as in steps 1, 2, and 3 of Single Flare Project.

- Insert tubing through correct size hole so that the cut off end of tube extends beyond surface of flaring bar to proper distance, determined by corresponding size adapter.

- Tighten wing nuts securely, starting with the wing nut nearest the tubing.

- Insert stem of adapter into the end of the tubing.

- Place yoke assembly over flaring bar and adapter, so cone enters the depression in the end of adapter.

- With the sliding T-handle, turn and force cone down until adapter rest flat against bell shape of tubing so the tube folds in on itself.  Back off cone and remove adapter from tubing.

- With adapter removed place cone of yoke assembly directly in the tube opening and tighten T-handle until cone bottoms out.  Make sure the cone and yoke are STRAIGHT up and down or the flare will be defective.

- Back off cone and remove yoke assembly and inspect flare.

- Show your instructor

Assignment:

- What are two advantages of double flaring as compared to single flaring?

- How is tubing size determine.

- Give three types of tubing and tell where they could be used.

- What precaution is built in to every flared fitting to guarantee that parts of one cannot be interchanged with another or different design?

- What type of fitting does not require the tubing to be flared?