Disassemble and Assemble a Multi-Leaf Spring		X189

Reference:

- CDX eTextbook – Steering & Suspension – Suspension Systems – Leaf Springs

- Automotive Mechanics – Ch 49 p. 663

Equipment:

- “C”- clamp and two wrenches.

Procedure:

- Tighten “C”-clamp over the leaves of the spring adjacent to the centre bolt.

- Using the wrenches remove the centre bolt.

- Tighten the “C”-clamp over the leaves of the spring adjacent to one of the rebound clips.

- Using the wrenches remove the bolts holding the clip and then remove it.

- Repeat the procedure on the remaining clip.

CAUTION: 	If it is necessary to hammer the bolts out NEVER strike a bolt directly in the threaded end.  Turn a nut onto the bolt and strike it with a hammer.

- Use the “C”-clamp to compress the leaves in proper alignment and re-install the (1) Centre Bolt and then (2) the Rebound Clips.

Assignment:

1.  Define:	Unsprung Weight

Overslung spring

- State the purpose of:

  - “U” bolt

  - Centre Bolt

  - Swing Shackle

  - Stabilizer Bar

  - Shock Absorber